## Slide 1: Week 15-Lec 1
Data center Networking

## Slide 2: Data center networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center
Inside Facebook’s datacenter

## Slide 3
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)
Internet

## Slide 4: Connectivity
The hosts (blades)
  Include CPU, memory, and disk storage.
  Stacked in racks, with each rack typically having 20 to 40 blades.
  At the top of each rack there is a switch, Top of Rack (TOR) switch
    interconnects the hosts in the rack with each other and with other switches in the data center
    Each host has a NIC card that connects to its TOR switch,
    Each TOR switch has additional ports that can be connected to other switches.
hosts below each access router form a single subnet.
In order to localize ARP broadcast traffic,
  each of these subnets is further partitioned into smaller VLAN subnets
    each comprising a few hundred hosts

## Slide 5: Traffic types
traffic flowing between external clients and internal hosts
  One of more Border routers – Data center to public Internet
Traffic flowing between internal hosts
External requests directed to load balancer
  Distribute jobs/requests to servers
  Destination port num and IP address

## Slide 6
How
are
datacenter
networks
different
from
networks
we’ve seen
before?
Scale: very few local networks have so many machines in one place:
10’s of thousands of servers — and they all work together like one computer!
•
Control:
Internet, software
entirely administered by one organization — unlike the
•
datacenter owners control every switch in the
on every host
network and
the
Performance: datacenter latencies are 10s of us, with
100Gbit links.
10, 40, even
•
How do these factors change how we design datacenter
networks?

## Slide 7
Desirable
Properties
Low Latency: Very few “hops” between destinations
•
Resilience: Able to recover from link failures
•
Good Throughput: Lots of endpoints can communicate,
same time.
all at the
•
Cost-Effective: Does not rely too much on expensive equipment like
very high bandwidth, high port-count switches.
•
Easy to Manage: Won’t confuse network administrators who have to
wire so many cables together!
•

## Slide 8: Limitations: host-host capcacity

## Slide 9: Datacenter networks: multipath
9
10
11
12
13
14
15
16
two disjoint paths highlighted between racks 1 and 11
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 10: Datacenter networks: application-layer routing
…
…
…
…
…
…
…
…
Load
balancer
Internet
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)

## Slide 11: Datacenter networks: protocol innovations
link layer:
  RoCE: remote DMA (RDMA) over Converged Ethernet
transport layer:
  ECN (explicit congestion notification) used in transport-layer congestion control (DCTCP, DCQCN)
  experimentation with hop-by-hop (backpressure) congestion control
routing, management:
  SDN widely used within/among organizations’ datacenters
  place related services, data as close as possible (e.g., in same rack or nearby rack) to minimize tier-2, tier-1 communication
Google Networking: Infrastructure and Selected Challenges (Slides: https://networkingchannel.eu/google-networking-infrastructure-and-selected-challenges/

## Slide 12
Google’s Data center