## Slide 1: Week 7-Lec 3
IP protocol and IP addressing

## Slide 2: IP addressing: introduction
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 3: What is an IP address?

## Slide 4
Example Of Dotted Decimal
Notation
A 32-bit number in binary
10000000 00001010 00000010 00000011
The same
notation
32-bit
number expressed in
dotted
decimal
128 . 10 . 2 . 3
22
Internetworking With TCP/IP vol 1
-- Part 4
2005

## Slide 5: What comprises an IP address?
Set of decimal numbers
192.168.123.132
What can we understand from this?
  NOTHING
How do routers interpret this decimal number?
  Set of binary digits
  1100000010101000111101110000100
  Can we make sense of it now?
Break the bunch of bits into 4 parts (8 bits each)
  11000000. 10101000.01111011.10000100
  Subnet Mask: local or remote network?
  11000000.10101000.01111011.10000100
  11111111. 11111111. 11111111. 00000000
  -------------------------------------------------------
11000000. 10101000. 01111011.00000000
------------------------------------------------------
  Network part: 192.168.123.0 (all 1s in the mask)
  Host part:0.0.0.132 (all 0s in the mask)

## Slide 6: IP addresses
How are addresses configured?
  Manually
  DHCP (server)
What are the requirements for assigning IP addresses to machines?
  # Hosts
  # Networks
Who gives a block of addresses to organizations?
  ICANN: Internet Corporation for Assigned
  Names and Numbers http://www.icann.org/
    allocates addresses
    manages DNS
    assigns domain names, resolves disputes

## Slide 7: Classes in IP addresses
Number of networks
Number of hosts
Class
Lowest Address
Highest Address
A
B
C
D
E
1.0.0.0
128.1.0.0
192.0.1.0
224.0.0.0
240.0.0.0
126.0.0.0
191.255.0.0
223.255.255.0
239.255.255.255
255.255.255.254

## Slide 8: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits

## Slide 9: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24

## Slide 10: Subnets
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24

## Slide 11: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 12: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 14: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8